Department of Computer Engineering

School of Electrical Engineering

University of Belgrade

POB 816

11000 Belgrade

Yugoslavia

Multimedia Networking

and Synchronization

Author:	Slobodan Laskovi(

Advisors: 	Emil Jovanov & Veljko Milutinovi(

Based on:	Borko Furht, Stephen W. Smoliar, & HongJiang Zhang:

Video and Image Processing in Multimedia Systems

Chapter #2

E-mail:{ejovanoe,emilutiv}@etf.bg.ac.yu

Multimedia Networking and Synchronization

In a typical distributed multimedia application, multimedia data must be:

Compressed

Transmitted over the network to the destination

Decompressed and synchronized for playout at the receiving site

A multimedia information system must allow a user to:

Retrieve

Store

Manage

All above for a variety of data types including images, audio, and video.

Multimedia Networking Applications

Video mail

Videoconferencing

Collaborative work systems

All above requires networked multimedia.

| Information Type | Bit Rate | Quality And Remarks |
| --- | --- | --- |
| Data | Wide range of bit rates | Continuous, burst, and packet-oriented data |
| Text | Several Kbps | Higher bit rates for downloading of large volumes |
| Graphics |

Relatively low bit rates

Higher bit rates: (100 Mbps

Depending on the transfer time required

Exchange of the complex 3D computer model

Image

64 Kbps

Various

Up to 30 Mbps

Group-4 telefax

Corresponds to JPEG standard

High-quality professional images

Video

64-128 Kbps

348 Kbps - 2 Mbps

1.5 Mbps

5-10 Mbps

34/45 Mbps

50 Mbps

100 Mbps

Video telephony (H.261)

Videoconferencing (H.261)

MPEG-1

TV quality (MPEG-2)

TV distribution

HDTV quality

| Studio to studio HDTV video downloading |
| --- |
| Audio | nx64 Kbps | 3.1 KHz, 7.5 KHz, or hi-fi baseband signals |

Typical transmission rates of various information types in multimedia communication

Multimedia Networks:

Very high transfer rate or bandwidth 
(even when the data is compressed; see the table above)

Predictable transfer rate

Data transfer is:

Stream oriented

Highly bursty

Network load is long and continuous

Applications can tolerate errors in transmission due to corruption or packet loss
without retransmission or correction; in some cases some packets are even discarded

Lightweight transmission protocols

Low latency

Synchronized transmission with low jitter

Multipoint communications

Traditional Networks

Traditional networks do not suit multimedia!

Ethernet:

Only 10 Mbps bandwidth

Access time is not bounded

Latency and jitter are unpredictable

Token-ring:

16 Mbps bandwidth

Deterministic

Worst-case access latency can be very high

FDDI:

100 Mbps bandwidth

Low access latency

Low jitter in synchronized mode

Bounded access delay

Predictable average bandwidth for synchronous traffic

High cost

Less expensive alternatives:

Fast Ethernet (100 Mbps bandwidth)

Priority token-ring

Priority Token-Ring (PTR):

Multimedia traffic is separated from regular traffic by priority

Works on existing networks

The admission control in PTR guarantees bandwidth to multimedia sessions

Priority token ring in multimedia applications

Crimmins [Cri93] evaluated three priority ring schemes 
for their applicability to videoconferencing applications:

Equal priority for video and asynchronous packets

Permanent high priority for video packets

Time-adjusted high-priority for video packets (based on their ages)

Broadband Integrated Services Digital Network (B-ISDN):

Expected to become the key network for multimedia applications [Cla92]

Types of B-ISDN:

Basic ISDN, supports 2B + D channels,
where the transfer rate of a B channel is 63 Kbps,
and that of a D channel is 16 Kbps

Primary ISDN, supports 23B + D channels in US,
and 30B + D channels in Europe.

Asynchronous Transfer Mode

The architecture of an ATM network consists of a set of terminal nodes 
and a set of intermediate nodes (switches)

Asynchronous Transfer Mode (ATM) [Bou92, SVH91, KMF94, DCH94] 
is considered to be the network of the future:

Packet oriented

Uses a connection-oriented technology

An ATM network comprises of a set of terminals and a set of intermediate nodes (switches), all linked by a set of point-to-point ATM links

ATM standard defines the protocols needed to connect the terminal and the nodes; however, it does not specify how the switches are to be implemented

ATM Cells:

The basic transport unit in an ATM network

Cells are fixed length packets of 53 bytes

The header consists of the information necessary for routing:

The Generic Flow Control (GFC) field is used for congestion control

The User-to-Network Interface (UNI) to avoid overloading

The VirtualPath/ChannelIdentifier (VPI/VCI) fields 
contain the routing information

The Payload Type (PT) represents the type of information carried by the cell

The CLP field indicates cell loss priority

The Header Error Control (HEC) field is used to detect and correct header errors

| Bits | 7 |
| --- | --- |
| 0 | Bytes |
| Header | 5 Bytes |
| GFC | VPI | 0 |
|  | VPI |
|  | 1 |
|  | VCI | 2 |
| Payload | 48 Bytes |
|  | PT | CLP | 3 |
|  | HEC | 4 |
| (a) |
|  | (b) |

Components of: (a) ATM cell, (b) ATM header

The header does not contain the complete destination address

The cells are switched by a switching node using the routing tables

ATM Connections:

A connection has to be established between two end points
before data can be transmitted

A terminal requests a connection to another end terminal
by transmitting a signaling request across the UNI to the network

If the destination agrees to form a connection,
a virtual circuit is set up between these two end points

The connections are made of Virtual Channel (VC) and Virtual Path (VP) connections

Virtual connections in ATM

Connections are either point-to-point or point-to-multipoint

Virtual Channel is a logical connection between two switching points

VP is a group of VC’s with the same VPI value

An example of setting up a VC connection between two nodes N1 and N2:

The process of establishing the VC connection consists of the following steps:

The end terminal N1 sends the request to the UNI.

The UNI forwards the request to the network.

Assume that the network selects the following route A-B-C-D.
Each of the four nodes will use an unused VC value for the connection. 
For example, the intermediate node A chooses VC1, 
and therefore all the cells from N1 will have a label VC1 at the output from A.

Node A sends the cell to node B. 
B will change VC1 to VC2 and will send VC2 to node C.

At the node C, VC2 is associated with VC3 and sent to node D.

At the node D, VC3 is associated with VC4. 
The node D checks if the UNI at the terminal node N2 is free. 
If the UNI is free, the cell with the label VC4 is given to N2.

The terminal node N2 uses now VC4 for its connection to the node D.

D sends this cell to C, which associates VC4 with VC3, and sends the cell to B. 
B associates VC3 with VC2 and sends the cell to A. 
A associates VC2 with VC1 and delivers the cell to the terminal node N1.

The connection between terminal nodes N1 and N2 is thus established.

When the transmission of data is completed, 
N1 sends a message to tear down the connection

The cells within a VC are not switched out of order 
and no retransmission is done in ATM

End-to-end delay is not predictable, because of buffering at the source

ATM does not guarantee that a cell will be delivered to the destination 
(in the case of congestion)

Quality of Service (QOS) parameters: 
peak data rate, cell loss rate, cell delay, and cell delay variation

Connection is established only if the network support for QOS is requested by the user

An ATM connection between two terminal nodes N1 and N2.

Comparison of Switching Technologies for Multimedia Communications:

Besides the ATM technology, 
other switching technologies considered for multimedia communications include:

Synchronous Transfer Mode (STM),

Switched Multi-Megabit Data Service (SMDS), called 802.6, and

Frame Relay

STM:

Circuit switched network mechanism

Packetized voice and data transported over the networks

Bandwidth is allocated for the entire duration of the connection

The ATM network overcomes this limitation by using
statistical multiplexing with hardware switching

SMDS:

Uses a telecommunication network to connect LANs LAN into
Metropolitan Area Networks (MANs) and Wide Area Networks (WANs)

Frame Relay:

Similar to packet switching networks

Multiple virtual circuits on a single access line

Operates at higher data rates, 
and gives lower propagation delays than most packet networks

| Parameters | ATM | STM |
| --- | --- | --- |

SMDS

| (802.6) | Frame relay |
| --- | --- |
| Support of | Data | Yes | Yes | Yes | Yes |
| multimedia | Audio | Yes | Yes |
| traffic transfer | Video | Yes | Yes |
| Connectivity | One-to-many | Yes | Limited | Yes | Yes |
|  | Many-to-one | Yes | Limited | Yes | Yes |
|  | Many-to-many | Yes |
| Yes | Yes |
| Performance guarantee | Delay for audio/video | Yes | Yes |
|  | Packet loss for data | Yes | N/A | Yes | Yes |
| Bandwidth | 1.5 Mbps to multi Gbps | Few bits/s to multi Gbps | 1.5 Mbps to 45 Mbps | 56 Kbps to 1.5 Mbps |
| Guarantee of media synchronization | Yes | Yes |
| End-to-end delay | Low | Lower than ATM | Higher than ATM | Higher than ATM |
| Congestion control | Required | Not required | Required | Required |

Comparison of switching technologies for multimedia communications,
adapted from [RKK94]

Multimedia Synchronization

Multimedia systems include multiple sources of various media either spatially or temporally to create composite multimedia documents.

Spatial Composition:

Links various multimedia objects into a single entity

Includes object size, rotation, and placement

Spatial Composition

Temporal Composition:

Creates a multimedia presentation by arranging the multimedia objects 
according to temporal relationship

Temporal Composition

One can divide temporal composition, or synchronization, 
into continuos and point synchronization

Continuous Synchronization:

Constant synchronization of lengthy events

An example of continuos synchronization is video telephony,
where audio and video signals are created at a remote site,
transmitted over the network, 
then synchronized continuously at the receiver site for playback

Point Synchronization

A single point of one media block coincides with a single point of another media block

An example of point synchronization 
is a slide show with blocks of audio allotted to each slide

Two further classes of synchronization are serial and parallel synchronization

Serial Synchronization

Determines the rate at which events must occur within a single data stream
(intremedia synchronization)

Parallel Synchronization

Determines the relative schedule of separate synchronization streams
(intermedia synchronization)

Data Location Models

Responsibility for maintaining intermedial synchronization falls onto 
both the sources and destinations of data, 
but most techniques rely more on the destinations.

There are four data location models:

Local single source
As long as the devices maintain their playback speed, 
no synchronization technique is required.

Local multiple sources
An example is a slide show played with music or an audio tape. 
Synchronization is required within the workstation.

Distributed single source
An example is cable TV. 
The technique requires no synchronization 
other than maintaining the speeds of the playback devices.

Distributed multiple source
This group further breaks down into:

Multiple sources from one node distributed to another node
(for example, a video call)

Multiple sources from two or more nodes distributed to another node

Multiple sources from one node distributed to two or more nodes
(for example, hdtv)

Multiple sources from two or more nodes distributed to two or more nodes
(for example, a group teleconference).

The two cases with distributed sources require more complex synchronization algorithms to eliminate the various causes of asynchrony.

Various causes of asynchrony in a video telephone system

The end-to-end delay of a distributed multimedia system consists of 
all the delays crested at the source site, network, and receiver site.

FOR CONTINUOUS SYNCHRONIZATION

| Tsample | Tencode | Tpacketize | Ttransmit | Tbuffer | Tdepacketize | Tdecode | Tpresent |
| --- | --- | --- | --- | --- | --- | --- | --- |

FOR STORED OBJECTS (Remote Data Access)

| Tquery | Tseek | Taccess | Tpacketize | Ttransmit | Tbuffer | Tdepacketize | Tdecode | Tpresent |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Definitions of the end-to-end delay:
(a) for continuous synchronization, (b) for stored objects.

Quality of  Service

Implementing a synchronization algorithm for a specific application 
requires specifying the quality of service (QOS) for multimedia communications.

The QOS is a set of parameters that includes
speed ratio, utilization, average delay, jitter, bit error rate, and packet error rate [LG90]:

The speed ratio is the quotient of 
the actual presentation rate divided by the nominal presentation rate

The utilization ratio equals the actual presentation rate 
divided by the available delivery rate

Jitter is the instantaneous difference between two synchronized streams

Skew is the average difference in presentation times between two synchronized objects over n synchronized points (stream lag, stream lead).

Two more QOS parameters, 
the bit error rate (BER) and the packet error rate (PER), 
specify the required reliability of the network.

|  | Video telephony | JPEG video transmission |
| --- | --- | --- |
| Speed ratio | 1.0 | 1.0 |
| Utilization | 1.0 | 1.0 |
| Average delay | 0.25 sec | 0.2 sec |
| Minimum jitter | 10 msec | 5 msec |
| Maximum BER | 0.01 | 0.1 |
| Maximum PER | 0.001 | 0.01 |

Quality of service requirements for video telephony and JPEG video transmission

Single and Multiple Stream Synchronization:

Synchronization entails evaluating the temporal characteristics of the data streams to be synchronized and correcting all delays and other anomalies [LG91]

To synchronize an event, we first analyze the end-to-end delay, or latency;
Then we schedule a retrieval time that allows enough time before the deadline
to allow for latency

For example, if the total latency time of retrieving a one-hour video is three minutes, 
and the customer ordered the video for 7 P.M.,
set the retrieval time, or the packet production time, for 6:57 P.M. at the latest.

Timing for the single-event synchronization