Department of Computer Engineering

School of Electrical Engineering

University of Belgrade

POB 816

11000 Belgrade

Yugoslavia

Implementations of Compression Algorithms

Author:	Vladan Andrijani(

Advisors: 	Emil Jovanov & Veljko Milutinovi(

Based on:	Borko Furht, Stephen W. Smoliar, & HongJiang Zhang:

Video and Image Processing in Multimedia Systems

Chapter #9

E-mail:{ejovanoe,emilutiv}@etf.bg.ac.yu

How to partition between hardware and software

to maximize performance and  minimize cost

The present solutions use video compression chips and DSPs on PC backplanes

In the future, processors will perform real-time compression and decompression in software

Implementations of Compression Algorithms:

1. Single-function processors  (the first generation of compression chips)

Implement the most demanding operations of algorithms

such as DCT, motion estimation and quantization

Examples include compression chips from C-Cube, LSI Logic, and SGS-Thompson

2. Multi-standard compression chips (the second generation of compression chips)

Integrate programmable processors

Examples include compression chips from IIT, Array Microsystems, and C-Cube

3. Software solution and a general purpose processor

Maximize flexibility and reduce cost

Examples include Apple Video, Microsoft Video, and Intel Indeo

Software JPEG Systems

The best performance in terms of speed was achieved with the Optivision 5250

Autograph International (AGI) offers JPEG compression software called EasyTech/Codec

Various JPEG compression programs for DOS and Windows have been tested in [Rau92]

The best results were obtained using Alice-DOS utility from Telephoto

The best pure software JPEG has been LeadView 1.7 from Lead Technologies

Video Compression Software

Intel Indeo uses the following software compression techniques:

Color subsampling

Reduction from 24 bits/pixel to an average of 9 bits/pixel

Pixel differencing

Elimination of redundant data between two frames by comparing  their  pixels

Run length encoding-RLE

RLE is used only when resulting difference between adjacent  pixels is zero

RLE encodes the zero value and a count of consecutive zero values

Vector quantization-VQ

VQ is used when the difference between adjacent pixels is very close to zero

5. Variable content encoding-VCE is a statistical compression technique

VCE compresses the difference values by assigning variable length codes to them

General-purpose processors’

support for MPEG decoding

Design for asymmetric multimedia applications

Designed to support real-time MPEG decoding and other multimedia functions

Examples include three advanced processors:

1. UltraSPARC V9 (SUN)

2. PA-RISC 7100LC (Hewlett-Packard)

3. PowerPC 620 (Motorola)

PowerPC 620

- Specifically designed for distributed multimedia systems

- Supports both CPU-intensive and I/O-intensive applications

- Can be used both for multimedia servers and multimedia workstations

UltraSPARC V9 and Its Visual Instruction Set (VIS)

Supports new data types:

1. Pixels (four 8-bit unsigned integers contained in a 32 bit word)

2. Fixed data (four 16-bit or two 32-bit fixed point components contained in a 64-bit word)

New classes of instructions:

1. Conversation instructions (convert between various formats)

2. The motion estimation instruction-PixelDISTance

- Computes the sum of the absolute differences between two 8 pixel vectors

- Accumulating the error for 16x16 block

requires 32 PDIST or 1500 conventional instructions

VIS provides four times or higher speed-up for most of the time-critical computations

UltraSPARC is capable

of decoding MPEG-2 video of 720x480 pixels with resolution of 30 frames/sec