Department of Computer Engineering

School of Electrical Engineering

University of Belgrade

POB 816

11000 Belgrade

Yugoslavia

The JPEG Algorithm

for Full-Color Still Image Compression

Author:	Sa(a Slijep(evi(

Advisors: 	Emil Jovanov & Veljko Milutinovi(

Based on:	Borko Furht, Stephen W. Smoliar, & HongJiang Zhang:

Video and Image Processing in Multimedia Systems

Chapter #5

E-mail:{ejovanoe,emilutiv}@ubbg.etf.bg.ac.yu

JPEG Algorithm

·	Targeted for full-collor still frame applications

·	Four modes:

Sequential direct cosine transformation (DCT)-based encoding,

in which the image is encoded in a single scan

Progressive DCT-based encoding,

in which the image is encoded in multiple scans

Lossless encoding,

which guarantees the exact reproduction

Hierarchical encoding,

in which the image is encoded in multiple resolutions

An JPEG  Encoder

·	Image is divided into the appropriate number of 8x8 blocks

Range Shift

·	Original samples are shifted from range [0,2P-1] to range [-2P-1,2P-1-1]

In this example: P=8

for  ,   for

for  ,       for

Components of the transformed block are called DCT coefficients

Coefficient F(0,0), whose position is in the left-top corner of the block

is called DC coefficient,

and others are called AC coefficients

For a greyscale image, DCT coefficients are in the range [-1024,1023],

and its representation requires additional 3 bits, compared to the original samples

Most coefficients have zero or nearzero values,

and that is the foundation for compression

Quantization

Q (u , v)

Quantization table is specified by applications

Quantization table in this example is proposed in (Nel 92(:

for (i=0;i<N;i++)

for (j=0;j<N;j++)

Q ( i , j )=1+((1+i+j) x  quality)(

Parameter quality specifies the quality factor and its recommended range is from 1 to 25

In this example, it is used quality=2

Quality=1 gives the best quality, but the lowest compression ratio,

and quality=25 gives the worst quality and the highest compression ratio

Quantization increases the number of zero-valued coefficients

Loss of information from the quantization is not visually significant

There is usually a strong correlation between DC coefficients of adjacent 8x8 blocks,        and DC coefficients used for predictive coding

AC coefficients are ordered into a “zig-zag” sequence,

what will help to facilitate the entropy encoding

Huffman Coding

RUNLENGTH is the number of consecutive zero-valued AC coefficients

preceding the non-zero AC coefficient

SIZE is the number of bits for encoding amplitude

AMPLITUDE is the amplitude of the non-zero AC coefficient

Example: 0,0,0,0,0,0,476 is (6,9)(476)

Symbol (0,0) means “End Of Block” (EOB) and terminates each 8x8 block

Binary sequence is generated using the Huffman table

An JPEG Decoder

All steps from the encoding process are inversed and implemented in reverse order

The binary sequence is converted to a symbol sequence using Huffman tables,

and then the symbols are converted into DCT coefficients

Dequantization is implemented using the following function:

Inversed discrete cosine transformation (IDCT) is implemented using the equation:

for  ,   for

for  ,       for

The last step consists of shifting back the decompressed samples in the range [0,2p -1]

Compression Measures

Compression ratio (Cr)

Higher Cr produce lower picture quality and vice versa

Number of bits per pixel in the compressed image (Nb)

Root Mean Square (RMS) error

-  original pixel values

-   pixel values after decompression

n   -   total number of pixels in an image

JPEG Compression of Color Images

JPEG sorce image model consists of 1 to 255 image components,

called color or spectral bands

For example, RGB representation consists of three color components

Each component may have a different number of pixels

in the horizontal (Xi) and the vertical (Yi) axis:

First example is with the same resolutions,

and second example is with the different resolutions

The color components can be processed in two ways:

Non-interleaved data ordering, in which processing is performed

component by component from left-to-right and top-to-bottom

Interleaved data ordering, in which different components are combined

into so-called minimum code units (MCUs)

Interleaved data ordering is used for applications that need to display or print                multiple-component images in parallel with their decompression

Example of interleaved data ordering

A:  H=2 ,  V=2                           B:  H=2 ,  V=1                 C:  H=1 , V=2     D:  H=1 ,  V=1

DATA  UNITS                    A                         B                      C                     D

MCU1 =  ( A00, A01, A10, A11,    B00, B01,        C00, C10,           D00 )

MCU2 =  ( A02, A03, A12, A13,    B02, B03,        C01, C11,           D01 )

MCU3 =  ( A04, A05, A14, A15,    B04, B05,        C02, C12,           D02 )

MCU4 =  ( A20, A21, A30, A31,    B10, B11,        C20, C30,           D10 )

The first block in the encoder and last block in the decoder for color JPEG compression            is a color space conversion block, such as RGB to YUV, and vice versa

JPEG algorithm spends 42% of compression time performing FDCT,                                 and 48% of decompression time performing IDCT

An example of the JPEG color compression (320 x 240 image, 24 bits/pixel)                             on an i486/33MHz machine with no math coprocessor

Progressive JPEG Compression

In some applications, an image may have large number of pixels

and the decompression process and transmission may take several minutes

The progressive JPEG mode quickly produces a rough image,

and then improves its quality using multiple scans

The progressive JPEG encoder must have an additional buffer

at the output of the quantizer and before the entropy encoder

Progressive JPEG compression can be achieved using three algorithms:

Progressive spectral selection algorithm,

Progressive successive approximation algorithm,

Combined progressive algorithm.

Progressive Spectral Selection Algorithm

The DCT coefficients are grouped into several spectral bands

Low-frequency DCT coefficient bands are sent first,

and then higher-frequency ones

Progressive Successive Approximation Algorithm

DCT coefficients are sent first with lower precision, and then refined in later scans

Combined Progressive Algorithm

Combines spectral selection and successive approximation algorithm

Sequential Lossless Jpeg Compression

Prediction block has replaced the FDCT and the quantization block

from the baseline sequential DCT-based JPEG encoder

A prediction  of the sample X is calculated on the basis of previous samples A, B and C

Predictor formula can as be simple as =A or as complex as =B+(A-C)/2

Hierarchical JPEG Compression

Hierarchical JPEG mode creates a set of compressed images

beginning with small images, and then continuing with images of increased resolutions

Lower resolution image is scaled up to the next resolution                                                  and used as a prediction for the following stage