Department of Computer Engineering

School of Electrical Engineering

University of Belgrade

POB 816

11000 Belgrade

Yugoslavia

Other Multimedia

Compression Techniques

Author:	Dejan Ostojiæ

Advisors: 	Emil Jovanov & Veljko Milutinoviæ

Based on:	Borko Furht, Stephen W. Smoliar, & HongJiang Zhang:

Video and Image Processing in Multimedia Systems

Chapter #8

E-mail:{ejovanoe,emilutiv}@etf.bg.ac.yu

Compression Techniques

Digital Video Interactive (DVI) technology

Fractal image compression

Subband image and video coding

Wavelet-based compression

Digital Video Interactive

(DVI) Technology

The DVI system has been implemented using two specially-designed processors:

82750PB pixel processor (PB)

Image compression and decompression

Generates fast graphics and special effects

Acts as the arbiter of memory

Includes ALU, barrel shifter, pixel interpolator, and statistical decoder

82750DB display processor (DB)

Various real-time display functions

Provides outputs to the display devices

DVI technology performs its operations in an internal YUV format

DVI Compression Algorithm (Production Level Video)

The key algorithm for DVI compression is the Production Level Video (PLV)

The PLV algorithm is based on motion-compensated prediction and vector quantization

DVI decoder interpolates between pixel values in the previous frame 
to derive the starting point in the current frame

The decoder constructs the array of signed difference pixels 
and adds them to the motions-compensated array to make the final reconstructed region

PB is decoding process using four instructions for every two pixels

Interframe motion-compensated vector quantization implemented in DVI

Fractal Image Compression

Fractal is an infinitely magnifiable picture
 that can be produced by a small set of instructions and data

The fractal compression is based on

Breaking an image into pieces (fractals)

Identifying fractals which are similar or identical

Doing affine transformations, which is a mathematical function consisting of 
a combination of rotation, scaling, skew, and translation in n-dimensional space

determines the rotation,

skew, scaling

detrmines the translation

An algorithm for the fractal compression

An algorithm for the fractal decompression

Subband Image and Video Coding

Subband coding is based on splitting the input signals into smaller frequency bands; these subbands are then encoded, transmitted or stored, 
and later reconstructed using decoded subbands

The method for image and video subband coding is a 2D Quadrature Mirror Filtering (QMF)

The 2D QMF is performed applaying 1D QMF along the rows and then 
along the columns

The separability characteristics, specified as:

H1 (z1,z2) = H11 (z1) H12 (z2)

reduces 2D QMF filtering problem into 1D filtering

Subband Coding of Images

The input image is first split into subbands using the subband transform technique, 
and then the subbands are encoded using commonly used techniques such as PCM, DPCM

Subband encoder of images

Subband Coding of Video Signals

The block diagram of the motion-compensated interframe subband encoder

Wavelet-Based Compression

Wavelet transform is a type of signal representation which can give 
the frequency content of the signal at a particular instant of time

One of the possible implementations of wavelet transform: using QMF

The wavelet-based compression consist of three steps:

Forward wavelet transform to decorrelate the image data

Quantization of the transform coefficients

Encoding the quantized coefficients

Wavelet transform is a type of signal representation 
which can give the frequency content of the signal at a particular instant of time

The block diagrams of the wavelet-based compressor and decompressor