Department of Computer Engineering

School of Electrical Engineering

University of Belgrade

POB 816

11000 Belgrade

Yugoslavia

The MPEG Compression

for Motion-Intensive Applications

Author:	Nela Tom(a

Advisors: 	Emil Jovanov & Veljko Milutinovi(

Based on:	Borko Furht, Stephen W. Smoliar, & HongJiang Zhang:

Video and Image Processing in Multimedia Systems

Chapter #7

E-mail:{ejovanoe,emilutiv}@etf.bg.ac.yu

The MPEG compression algorithm

Compression of full-motion video

Interframe compression

Maximum compression rates of 200:1 through storing the differences between two frames

Compression of audio data at ratios ranging from 5:1 to 10:1

Intended for both asymmetric and symmetric applications

- Asymmetric: Frequent use of the decompression process; compression only once

- Symmetric: Equal use of the compression and decompression

The MPEG standard

1. Synchronization and multiplexing of video and audio

2. Video

3. Audio

The MPEG standards

MPEG-1 	for interactive multimedia and broadcast television

MPEG-2 	for supporting the interlaced video formats and a number of features for HDTV

and video communications over ISDN networks using ATM [Ste94,LeG91]

MPEG-4 	for interactive multimedia and video telephony [Ste94]

Parameters of MPEG standards

MPEG Video Encoder and Decoder

Frame Structures

MPEG sequence of frames for transmission: {1,5,2,3,4,9,6,7,8}

Types of frames in the MPEG standard

I frames (intra images)

Self-contained and coded using a DCT-based technique 
similar to JPEG

Lowest compression ratio within MPEG

P frames (predicted images)

Coded using forward predictive coding  -

actual frame is coded with reference to a previous frame (I or P)

Compression ratio is significantly higher than of I frames

B frames (bidirectional or interpolated images)

Coded using two reference frames, a past and a future frame 
(which can be I or P frames)

Highest amount of compression

Motion Estimation

Forward prediction	( 	B = A

Backward prediction 	( 	B = C

Interpolation              	( 	B = (A + C) / 2

Motion compensated interpolation implemented in MPEG

Motion estimator

Finds the best matching block in the available reference frames

Used to extract the motion information from the video sequence

For every 16 x 16 block of  P and B frames, one or two motion vectors are calculated

The search area in block-matching techniques for motion vector estimation:

(a) a general case, (b) a typical case for MPEG: n = m =16, p = 6

F-a macroblock in current frame, G-search area in a previous (or future) frame

Cost Functions

Mean-Absolute Difference MAD:

Mean-Squared Difference MSD:

Cross-Correlation Function CCF:

F(i,j) - represents a (m x n) macroblock from the current frame

G(i,j) - represents the same macroblock from a reference frame

(dx,dy) - a vector representing the search location

The search space is specified by: dx = {-p,+p} and dy = {-p,+p}

Reduction of Computational Complexity

Pixel Difference Classification PDC [GM90]:

;		 (dx,dy) = {-p, +p}

Search Algorithms

1. The exhaustive search algorithm

Simplest but computationally intensive: for MSD function, it gives 169 iterations

2. The three-step motion vector estimation algorithm: [K+81], [L+94]

For MSD function, it gives 25 iterations

3. The modified 2D logarithmic search algorithm: [JJ81], [SR85]

For MAD function, it gives maximum 19 iterations

4. The conjugate-direction search method for motion vector estimation: [SR85]

It can be implemented as an one-at-a-time search method

5. The parallel hierarchical 1-D search algorithm (PHODS): [C+91]

Reduces the number of blocks to be searched

6. The modified pixel-difference classification, layered structure  (MPDC-LSA): [C+94]

Gives low computational complexity

The three-step motion vector estimation algorithm - an example

The modified 2D logarithmic search algorithm - an example

The conjugate-direction search method for motion vector estimation - an example

Audio Encoder and Decoder

The block diagram of a typical MPEG-1 encoder

The block diagram of a typical MPEG-1 decoder

Block diagrams of the MPEG audio encoder and decoder

The MPEG Data Stream

Layers of the MPEG video stream syntax

The MPEG Experimental Results

Berkeley MPEG-1 Software Decoder

Written in C

RISC workstations, X-Windows system

Decode and play 160 x 120 MPEG-1 video streams in real-time (30 frames/sec)

Berkeley MPEG-1 software decoder - analysis of execution times [PSR93]

Hewlett-Packard MPEG-1 Software Decoder

Written in C

Implemented on PA-RISC processor

Decompression of MPEG-1 videos in real-time (30 frames/sec)

PA-7100LC processor

Central processor of the HP712 desktop computer

PA-RISC architectural enhancement

New multimedia instructions, allow simple arithmetic operations to be executed in parallel

Two ALUs allow parallelism of four 16-bit operations per cycle

Reduces the display operation in the MPEG decoding

Reduces the overhead in the memory to frame buffer bandwidth

Comparison of various processors running the MPEG-1 software decoder [Lee95]