Department of Computer Engineering

School of Electrical Engineering

University of Belgrade

POB 816

11000 Belgrade

Yugoslavia

The PX64 Compression Algorithm

for Video Telecommunications

Author:	Nebojsa Gogic

Advisors: 	Emil Jovanov & Veljko Milutinovic

Based on:	Borko Furht, Stephen W. Smoliar, & HongJiang Zhang:

Video and Image Processing in Multimedia Systems

Chapter #6

E-mail:{ejovanoe,emilutiv}@etf.bg.ac.yu

The PX64 Compression Algorithm

Applications of the PX64

Desktop face-to-face visual communications (for channel capacity p=1)

Video Conferencing (for channel capacity p6)

The CCITT Video Format

Common Intermediate Format (CIF)

Quarter-CIF

CIF                                         QCIF

Lines/frame          Pixels/line     Lines/frame          Pixels/line

Luminance  (Y)            288                      352           144                       176

Chrominance  (Cb)      144                      176              72                          88

Chrominance  (Cb)      144                      176              72                          88

Parameters of  the CCITT Video Formats

Example 1: Desktop Videophone

Channel capacity:            p= 1

Network bandwidth:        BA= 64kbits/sec

Format:                            QCIF

Frame rate:                      10frames/sec

Required number of bits: Nb= (144×176 + 72×88 + 72×88 )×8bits= 300Kbits/frame

Required bandwidth:         Br = 300Kbits/frame×10frames/sec= 3Mb/sec

Minimum compression ratio:

Example 2: Video Conferencing

Channel capacity:            p= 10

Network bandwidth:        BA= 640Kbits/sec

Format:                            CIF

Frame rate:                      30frames/sec

Required number of bits: Nb= (288×352 +144×176 + 144×176)×8bits=1.21Mb/frame

Required bandwidth:       Br= 1.21Mb/frame×30frames/sec= 36.4Mb/sec

Minimum compression ratio:

The PX64 Encoder and Decoder

Algorithm Structure

DCT-based intraframe compression, using DCT quantization and entropy coding,
  similarly to JPEG

Predictive interframe coding based on Differential Pulse Code Modulation (DPCM) 
  and motion estimation

Video in

DCT               Quantizer

Dequantizer

IDCT                 Motion

vector

Predictor

frame memory

Block diagram of the PX64 encoder

Techniques of the Interframe Coding:

DPCM coding with no compensation (zero-motion vectors)

DPCM coding with non-zero motion vectors

Blocks are filtered by an optional predefined filter, to remove high-frequency noise

Previous frame 					 Current frame

Best match

The principe of interframe coding in the PX64 video compression

Buffer

Block diagram of the PX64 decoder

Video Data Structure:

A macro block:

four (8 x 8) luminance blocks and two (8 x 8) chrominance (Cr and Cb) blocks

A group of blocks is composed of 3 x 11Mbs

A CIF picture contains 12 GOB

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x       x-Luminance

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x         -Chrominance

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

x    x    x     x   x    x   x    x    x    x    x     x    x     x    x    x

Composition of a macro block: MB = 4Y+Cb+Cr

1    2                                                                        MB= 4Y + Cb + Cr

3    4

Y                      Cb                           Cr

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 |
| 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 |

1         2                                              1

3         4                                              2        QCIF= 3 GOBs

5         6                                              3

7         8     CIF= 12 GOBs

9       10

11       12

Hierarchical block structure of the PX64 data stream

GOB= 3×11  MBs

# Text boxes

Commpressed video stream

Video

multiplex

coder

(Huffman)

filter on / of

VLC decoder

Inverse
quantizer

IDCT

Reproduced image

Buffer

Received

bit stream

Motion-

compensation

predictor

frame memory

Filter

6

5